## Slide 1: NEUROPROSTHETIC GRASPING IMPROVEMENT USING sEMG AND DEEP GENERATIVE MODELING Advanced Deep Learning For Robotics
María Romeo Tricas – Jaume Gual Ramon
Dominik Winkelbauer

## Slide 2: INTRODUCTION AND MOTIVATION
Abandon rate of neuroprosthetic devices for upper limb amputees  ≈ 50%
Due to:
  Difficulties in usage control and grasping selection
Upper limb neuroprosthetic
Myoelectric hand graspings
Grasping selection is done with a switch…

## Slide 3: INTRODUCTION AND MOTIVATION
Our idea?
To develop a reliable and robust pipeline for generating graspings
Ease neuroprosthetics usage
  Attending to the user needs with sEMG Through generative modeling

## Slide 4: emg
What is EMG?
Electromyography is the graphic recording technique of electrical activity produced by skeletal muscles.
sEMG is obtained with surface electrodes on the muscles
Why EMG?
It is cheap, and it is non-invasive for users

## Slide 5: PIPELINE – 2 stages
sEMG Signals
Feature extraction
ResNet-18 DL Classifier
Main Grasping Type
E.g. cylindrical
User selects grasping intention through EMG

## Slide 6: PIPELINE – 2 stages
sEMG Signals
Main Grasping Type
E.g. cylindrical
User selects grasping intention through EMG
Extract 3D parameters of the object

## Slide 7: PIPELINE – 2 stages
sEMG Signals
Main Grasping Type
E.g. cylindrical
User selects grasping intention through EMG
Extract 3D parameters of the object
Diffusion Model
User wants… “cylindrical grasping”
Bottle has… “characteristics”
Fine-tuned hand pose

## Slide 8: PIPELINE – 2 stages
User selects grasping intention through EMG
Many different cups
Extract cup parameters
and create 3D model
Deep Generative Modeling Architecture
Fine-tuned grasp for the desired object 

## Slide 9: PIPELINE – 2 stages
User selects grasping intention through EMG
Many different cups
Extract cup parameters
and create 3D model
Deep Generative Modeling Architecture
Fine-tuned grasp for the desired object 

## Slide 10: PIPELINE – 2 stages
User selects grasping intention through EMG
DexGraspNet
Dataset with +5.000 objects, and +1.3 M grasps
Compare T,R,Θ
Deep Generative Modeling Architecture
Inputs
Ground truth

## Slide 11: First stage – emg classification

## Slide 12: Technical outline RECAP – emg classification
User performs 6 grasps
Raw sEMG is recorded and processed
Spectrograms (2 per trial)
Grasp types
Power grasp d) Palm
Hook e) Sphere
Lateral f) Tip
ResNet-18, 18 layers
User wants… “cylindrical grasping”

## Slide 13: Results – emg classification
Source | Average (N=5) | Reference
Testing Accuracy | 95.5 | 99.5
Recall | 95.5 | 99.6
Precision | 94.9 | -
F1-Score | 94.7 | 99.6
Our results vs. Reference paper

## Slide 14: Results – emg classification
Cyl
Hook
Lateral
Palmar
Sphere
Tip
40
39
43
42
56
40
1
2
4
1
1
1

## Slide 15: Technical outline – emg Dataset
450 samples per grasping  2700 samples
Stack of 2 RGB images  [480 X 640 X 6]
Split  80% - 10% - 10%

## Slide 16: Classifier – Resnet-18
Batch size | 10
Epochs | 40
Learning rate | 0.001
Momentum | 0.9
Residual Block
ResNet-18, 18 layers
Hyperparameters
Optimizer: SGD + Momentum
Loss function: CE Loss

## Slide 17: Technical outline – diffusion model
First part:
  sEMG classification provided good results  similar to the reference paper
  Future steps:
    Extend sEMG dataset to more grasping types

## Slide 18: Technical outline – diffusion model
First part:
  sEMG classification provided good results  similar to the reference paper
  Future steps:
    Extend sEMG dataset to more grasping types

## Slide 19: Discussion and future work
First part:
  sEMG classification provided good results  similar to the reference paper
  Future steps:
    Extend sEMG dataset to more grasping types
    Feed raw EMG to model  improvement in real-time performance
DL Classifier for Grasping Selection
Less computation than spectrograms!

## Slide 20: Discussion and future work
Second part:
  Investigate DexGraspnet
  Implement new pipeline

## Slide 21: second stage – generative modeling

## Slide 22: Technical outline – diffusion DATASET
Original Dataset – DexGraspNet
Large-Scale Robotic Dexterous Grasp Dataset for General Objects Based on Simulation
5.000 CAD objects
and
1.3 M generated grasps
Each grasp consisted of
22 joint angles (e.g. MCP)
3 wrist rotation angles
position of wrist in space

## Slide 23: Technical outline – diffusion DATASET
DexGraspNet
Selected reference grasps
Parameters:
Cylindrical
Planar
Spherical

## Slide 24: Technical outline – diffusion DATASET
Selected reference grasps
Cylindrical
Random dataset object + all grasps
DexGraspNet
Parameters:
Euclidean distance for 28 dimensions of grasp

## Slide 25: Technical outline – diffusion DATASET
Selected reference grasps
Cylindrical
Random dataset object + all grasps
DexGraspNet
Parameters:
Euclidean distance for 28 dimensions of grasp

## Slide 26: Technical outline – diffusion DATASET
Selected reference grasps
Cylindrical
Refined Dataset
DexGraspNet
Parameters:
1.000 objects and 21.000 grasps
… … …

## Slide 27: Technical outline – diffusion model
Refined Dataset
Object embedding: Euclidean distance map
Grasp embedding:
Joint angles
Grasp type:
One-hot vector
E.g., “cyl” = (1,0,0)

## Slide 28: Technical outline – diffusion model
DIFFUSION MODEL
Object embedding: Euclidean distance map
Grasp type:
One-hot vector
E.g., “cyl” = (1,0,0)
Grasp embedding:
Joint angles
Each Sample
Input
Output
Finetuned Grasp
Conditioned on:
Desired grasp type
Input object

## Slide 29: Technical outline – diffusion model
1: select a grasping for each grasp type from the DexGraspNet dataset
2: Create our dataset: look for the closer graspings (Euclidean Distance) for 1000 random objects. Each entry of our dataset: joint angles + trans + rot, type of grasping, mesh of distances.
3: prepare our diffusion model with inputs: joint angles + trans + rot, type of grasping, mesh of distances. Output: joint angles + trans + rot (28-dim).
4: Train our diffusion model (aqui explicar todos los pasos… 1 overfitting without object to 1 sample (solution: higher batch size and training longer), 2 overfitting with object, 3 overfitting for two samples, 4 training on full model (problem: translation y rotation), 5 training only on translation y rotation.

## Slide 30: Diffusion model - characteristics
INPUT
Object embedding
Grasp type:
Grasp embedding:
)
Timesteps embedding:
Euclidean distance map
Grasp type:
One-hot vector
E.g., “cyl” = (1,0,0)
Joint angles:
Timesteps vector:
CONV3D
POSITIONAL EMBEDDING
POSITIONAL EMBEDDING

## Slide 31: Diffusion model - characteristics
Batch size | 64
Epochs | 200 / 250
Learning rate | 1e-4 / 1e-5
Time steps | 50
β (diffusion rate) | ‘linear’
Embedding size | 64
Hyperparameters
INPUT
Object embedding
Grasp type:
Grasp embedding:
)
Time embedding:
Finetuned Grasp
OUTPUT
Optimizer: AdamW
Loss function: MSE Loss

## Slide 32: Diffusion model – TRAINING AND RESULTS
FULL MODEL
PLANAR GRASP
PLANAR GRASP
CYL GRASP
CYL GRASP

## Slide 33: Diffusion model – TRAINING AND RESULTS
FULL MODEL
Rotation and translation sometimes fails…

## Slide 34: Diffusion model – TRAINING AND RESULTS
ROTATION-TRANSLATION ONLY
PLANAR GRASP
PLANAR GRASP
CYL GRASP
CYL GRASP

## Slide 35: Discussion and future work
First part:
  sEMG classification provided good results  similar to the reference paper
  Future steps:
    Extend the sEMG dataset to more grasping types.

## Slide 36: Discussion and future work
Second part:
  Joint angles representation  almost PERFECT!
  Translation and rotation representation  not consistent at all!
   Dimensionality problem? Applying dimensionality reduction…
We also implemented dimensionality reduction with PCA:
   PCA did not achieve to represent the reconstructed sample properly.

## Slide 37: Discussion and future work
  Future steps:
  Implement different dimensionality reduction methods.
  Think about different approaches to solve this problem.

## Slide 38: NEUROPROSTHETIC GRASPING IMPROVEMENT USING sEMG AND DEEP GENERATIVE MODELING
María Romeo Tricas – Jaume Gual Ramon
Dominik Winkelbauer